## Slide 1: IP-XACT Tutorial
Richard Weber, Fellow, Director of Engineering Arteris
Anupam Bakshi, CEO, Agnisys

## Slide 2: Outline
Introduction
Component
Design and design configuration
Bus and abstraction definitions
Component bus interfaces and design interconnections
Component memory maps and registers
Component address spaces and bus interface bridges
Type definitions

## Slide 3: IEEE 1685 - IP-XACT, A Standard Structure …
For packaging IP
XML document format for IP data sheets
Design rules (SCRs), e.g., no overlapping registers
For integrating IP
XML document format for IP instances and their connections
Design rules (SCRs), e.g., no multiple drivers
For reusing IP within tool flows
Tool interface (TGI) to access XML data using web services
In practice, programming language specific APIs
Bus interfaces
Ports
Registers
Parameters
Views
Files
“Electronic IP Data Sheet”
IP instances
  Parameter values
Interconnect
“Electronic IC Data Sheet”
XML
Database
Generators

## Slide 4: IP-XACT Releases
The Spirit Consortium
IP-XACT 1.0 December 2004
IP-XACT 1.1 June 2005
IP-XACT 1.2 April 2006
IP-XACT 1.4 March 2008
IEEE Std. 1685-2009 December 2009
Accellera Systems Initiative
IEEE Std. 1685-2014 June 2014
IEEE Std. 1685-2022 September 2022
1.2: RTL
1.4: TLM & TGI
1685-2009: IEEE & Registers
1685-2014: - Mixed RTL and TLM - Conditionality - Parameter passing - Full TGI editing
1685-2022: - Type definitions - Structured ports - Component modes
- Mode-dependent access
- Power domains

## Slide 5: IP-XACT Document Types
Document types (also known as top-level elements)
component
design and design configuration
bus definition and abstraction definition
type definitions
abstractor
generator chain
catalog

## Slide 6: IP-XACT Document Identifier - VLNV
<?xml version="1.0" encoding="UTF-8"?> <ipxact:component xmlns:ipxact=http://www.accellera.org/XMLSchema/IPXACT/1685-2022 xmlns:xsi=http://www.w3.org/2001/XMLSchema-instance xsi:schemaLocation="http://www.accellera.org/XMLSchema/IPXACT/1685-2022 http://www.accellera.org/XMLSchema/IPXACT/1685-2022/index.xsd">
<ipxact:vendor>accellera.org</ipxact:vendor> <ipxact:library>i2s</ipxact:library> <ipxact:name>initiator_transmitter</ipxact:name> <ipxact:version>1.0</ipxact:version>
</ipxact:component>
Document type 
VLNV identifier 

## Slide 7: IP-XACT Catalog - VLNV Reference
<?xml version="1.0" encoding="UTF-8"?> <ipxact:catalog … > <ipxact:vendor>accellera.org</ipxact:vendor> <ipxact:library>ug</ipxact:library> <ipxact:name>my_catalog</ipxact:name> <ipxact:version>1.0</ipxact:version> <ipxact:components> <ipxact:ipxactFile> <ipxact:vlnv vendor="accellera.org" library="i2s" name="initiator_transmitter" version="1.0"/> <ipxact:name>../components/initiator_transmitter.xml</ipxact:name> </ipxact:ipxactFile> </ipxact: components > </ipxact:catalog>
The purpose of a catalog is to manage collections of IP-XACT files by documenting the location of IP-XACT files and the identifiers of the IP-XACT elements documented in those files.
Document type 
VLNV identifier 
VLNV reference 
File location 

## Slide 8: Component

## Slide 9: IP-XACT Component
The purpose of a component is to enable the (re-)use of an IP through IP-XACT without the need for information from the implementation files. To this end, a component documents aspects such as
the interfaces of an IP such as parameters, registers, ports, and grouping of ports into bus interfaces,
the views of an IP such as RTL and TLM descriptions, and
the files implementing each view, such as Verilog, VHDL, and SystemC files.

## Slide 10: Example IP-XACT Component
HDL
IP-XACT component
model 
An IP-XACT component model describes views, instantiations, and ports of the IP

## Slide 11: Example IP-XACT Component – Model (1)
An IP-XACT component view describes a “view” of the IP
view name 
reference to  component instantiation

## Slide 12: Example IP-XACT Component – Model (2)
language 
A componentInstantiation contains information to instantiate a module
library 
module 
module parameters 
reference to file set
parameters are specific for this module

## Slide 13: Example IP-XACT Component – Model (3)
A fileSet contains the files to compile a module
file set name 
list of files 

## Slide 14: Example IP-XACT Component – Model (4)
An IP-XACT component model describes the component ports
type is specific for this view
Notes: The wireTypeDef describes a view specific type name for port sd because the type “reg” is specific for the verilog language. For ports sck and ws, the type is the default type for any selected view; in this case “wire” since there is only one verilog view.

## Slide 15: Use cases for this example
From the HDL interface, one can automate
IP-XACT component generation
From the IP-XACT component, one can automate
human-readable document (data sheet) generation
compilation and elaboration
HDL interface generation

## Slide 16: Design

## Slide 17: IP-XACT Design
The purpose of a design is to describe the structure of a hierarchical IP and enable generation of views related to logical interconnect (e.g., system memory map) and physical interconnect (e.g., structural HDL). A design documents an internal structure of a component by describing
instances of sub-components that are used to implement a component,
parameter values for component instances, and
connections between component instances.

## Slide 18: Example IP-XACT Design
HDL
Schematic
IP-XACT Design

## Slide 19: IP-XACT Design – Component Instances
Component instances have an instance name and a VLNV reference

## Slide 20: IP-XACT Design – Ad Hoc Connections
Ad Hoc Connections reference internal or external ports of a net

## Slide 21: Design configuration

## Slide 22: IP-XACT Design Configuration
The purpose of a design configuration is to configure a design for a particular purpose by selecting an appropriate combination of views for its component instances. A design configuration documents a configuration of a design by describing
views that are used for component instances and
abstractor instances that are used for communication abstraction conversion on interconnections.

## Slide 23: Example IP-XACT Design Configuration
A view configuration selects a view for a component instance
instance name 
ref to view name 
view specific  parameter values

## Slide 24: Example IP-XACT Component – Hierarchical (1)
The view also references a designInstantiation and designConfigurationInstantiation

## Slide 25: Example IP-XACT Component – Hierarchical (2)
The view also references a designInstantiation and designConfigurationInstantiation

## Slide 26: Use cases for this example
From the HDL structure, one can automate
IP-XACT component, design, and design configuration generation
From the IP-XACT component, design and design configuration, one can automate
human-readable document (data sheet) generation
compilation and elaboration
physical connectivity generation (RTL/ESL structure, connectivity assertions)

## Slide 27: Bus and abstraction definition

## Slide 28: IP-XACT Bus Definition
The purpose of a bus definition and an abstraction definition is to describe aspects of a hardware communication protocol. A bus definition documents properties of a hardware communication protocol that are independent of the representation of the protocol such as
if direct connections between initiator and target interfaces are supported for a protocol
if the IP-XACT address calculations apply to a protocol to map target memory maps into initiator address spaces.
An abstraction definition documents a representation of a hardware communication protocol in terms of the logical ports and their properties such as direction and number of bits for initiator and target interfaces.

## Slide 29: Example Protocol - Inter-IC Sound (IIS or I2S)

## Slide 30: Example IP-XACT Bus Definition
<?xml version="1.0" encoding="UTF-8"?> <ipxact:busDefinition>
<ipxact:vendor>accellera.org</ipxact:vendor> <ipxact:library>i2s</ipxact:library> <ipxact:name>I2S</ipxact:name> <ipxact:version>1.1</ipxact:version>
<ipxact:description>I2S (Inter-IC Sound) bus definition</ipxact:description>
<ipxact:directConnection>true</ipxact:directConnection> <ipxact:isAddressable>false</ipxact:isAddressable>
</ipxact:busDefinition>

## Slide 31: Example IP-XACT abstraction definition (1)
An abstraction definition references a bus definition and describes the logical ports used in this representation of the protocol

## Slide 32: Example IP-XACT abstraction definition (2)
Logical port SCK
 SCK
 SCK
I
T

## Slide 33: Example IP-XACT abstraction definition (3)
Logical port WS
 SCK
 WS
 SCK
 WS
I
T

## Slide 34: Example IP-XACT abstraction definition (4)
Logical port SD_IN (naming _IN is based on initiator side)
 SCK
 WS
 SD_IN
 SCK
 WS
 SD_IN
I
T

## Slide 35: Example IP-XACT abstraction definition (4)
Logical port SD_IN (naming _IN is based on initiator side)
 SCK
 WS
 SD_IN
 SCK
 WS
 SD_IN
I
T
 SD_OUT
 SD_OUT

## Slide 36: Component bus interfaces and design interconnections

## Slide 37: Example Component Bus Interface (1)
A bus interface references a bus definition and an abstraction definition
This reference can be view specific.  different abstraction types for different views (see user guide for details on mixed- abstrction design)

## Slide 38: Example Component Bus Interface (2)
An abstraction definition provides logical ports on which the component ports shall be mapped
 sck - SCK
 ws - WS
 sd - SD_OUT

## Slide 39: Design Interconnections
u_target_receiver
u_initiator_transmitter
 sck - SCK
 ws - WS
 sd - SD_OUT
SCK - sck 
WS - ws 
SD_OUT - sd 
A design interconnection connects the mapped logical bits at its end points. Here:
SCK[0] connects to SCK[0]
WS[0] connects to WS[0]
SD_OUT[0] connects to SD_OUT[0]
Then the port maps are applied to get the physical connections:
sck connects to sck
ws connects to ws
sd connects to sd
I
T

## Slide 40: Example IP-XACT Design Interconnection
u_target_receiver
T
u_initiator_transmitter
I

## Slide 41: Design Interconnections
u_initiator_receiver
u_target_transmitter
 sck - SCK
 ws - WS
 sd - SD_IN
SCK - sck 
WS - ws 
SD_IN - sd 
I
T

## Slide 42: Design Interconnections
u_target_receiver
u_target_transmitter
 sck - SCK
 ws - WS
 sd - SD_IN
T
SCK - sck 
WS - ws 
SD_OUT - sd 
T
u_controller
SCK - sck 
WS - ws 
u_interconnect (phantom ports)
SCK
WS
SCK
WS
SD_IN
SCK
WS
SD_OUT
sck
ws
sd
I

## Slide 43: Component memory maps and registers

## Slide 44: Component memory map
A non-hierarchical addressable target bus interface shall reference a memory map and/or contain one or more transparent bridges
T
memory map
address block

## Slide 45: Address blocks, registers, and fields
A memory map may contain address block elements which may contain registers or register files with registers
A register contains at least one field
Fields may contain enumerated values

## Slide 46: Component address spaces and bus interface bridges

## Slide 47: Component address space
A non-hierarchical addressable initiator bus interface shall reference an address space
I
address space
segment
segment

## Slide 48: Mapping memory map into address space
address space
A design interconnection maps the memory map referenced by a target bus interface into the address space referenced by an initiator bus interface
I
T
memory map
address space
address block
segment
segment
address block

## Slide 49: Mapping address space into memory map ( transparent bridge )
A transparent bridge maps the address space referenced by an initiator bus interface into the memory map referenced by a target bus interface using the given base address offset
T
I
address space
memory map
bridge
address block
computed MM
address block

## Slide 50: Mapping address space into memory map ( subspace map - opaque bridge )
A subspace map maps the address space (segment) referenced by an initiator bus interface into the memory map referenced by a target bus interface using the given base address offset
T
I
address space
memory map (M)
subspace map (SM)
computed MM
segment of block
address block
segment (S)

## Slide 51: Elaborating system memory map (1/2)
T
T
I0
I
I1
T
B0
B1

## Slide 52: Elaborating system memory map (2/2)
B0
B1
B1
B0
B1
B0
B1
B0

## Slide 53: Type definitions

## Slide 54: Type definitions
The purpose of typeDefinitions is to enable re-use of memory map related elements by providing definitions for access policies, enumerations, register fields, registers, register files, address blocks, banks, memory maps, and memory remaps. Type definitions can be instantiated in other type definitions and in components as external type definitions. Elements in external type definitions can be referenced to describe (internal) memory maps or memory map elements.

## Slide 55: Example memory map definition
This typeDefinitions defines a memoryMapDefinition that contains an addressBlock.
The addressUnitBits value is parameterized

## Slide 56: Example memory map definition usage
This component instantiates an external typeDefinitions and sets its parameter values
The memory map references the memoryMapDefinition from the typeDefinitions

## Slide 57: Example fieldAccessPolicyDefinition
A fieldAccessPolicyDefinition defines register field access properties.
Example: UVM acces type W1C can be described as
and can be used in a fieldDefinition or field:

## Slide 58: Common Issues

## Slide 59: Common IP-XACT Issues
IP-XACT file does not pass xmllint with IP-XACT schema:
  xmllint –schema http://www.accellera.org/XMLSchema/IPXACT/1685-2022/index.xsd ip.xml
File does not pass IP-XACT SCRs
File does not contain register field volatile elements
  Volatile for fields is false when unspecified
  Example: read-only field without reset and with volatile false is unknown

## Slide 60: Thank you any questions?